## Slide 1: BCDA Cross Training
Love Controller Support
David Kline
April 4, 2005

## Slide 2: Contents
Overview,
Hardware Configurations,
Software Architecture,
  Common record initialization scenario,
  Read AI record scenario,
loveApp standalone application,
  Initialization scenario,
Reporting (dbior),
MEDM screens,
Distribution,
Improvements,
Acknowledgements,

## Slide 3: Overview
Love Controller,
  Instrument to measure voltage, current, thermocouple,
  Support models 1600 and 16A,
  Communication is through 2-wire RS485,
Device support,
  Old support based on MPF,
  New support based on Asyn,
  The echoServer and devMPC were departure points,
  Includes an interpose interface,
  Standalone application is available,
  IP-Octal RS232 and RS485 modules can be used,
Purpose of the new device support,
  Use as a learning tool for Asyn-based device support,
  Migrate from the unsupported MPF to Asyn,
  Appoint one as the owner of the module,
  Provide OS independence,

## Slide 4: Hardware Configuration – RS232 <-> RS485
MVME5100
Love
Controller
Model 16001
SBS XM-Octal-IO
Love
Controller
Model 16A2
Love
Controller
Model 1600n-1
Love
Controller
Model 1600n
B&B Electronics 485LDRC
Converter
B(+)
A(-)
RS485
RS232
TD
RD
TVME200
IP-OCTAL

## Slide 5: Hardware Configuration – RS485
MVME5100
Love
Controller
Model 16001
SBS XM-Octal-IO
Love
Controller
Model 16A2
Love
Controller
Model 1600n-1
Love
Controller
Model 1600n
B(+)
A(-)
TVME200
IP-OCTAL

## Slide 6: Software Architecture
Hardware Port
Lovelink Interpose Interface Layer (interposeLovelink)
Love Device Support (devAsynLove)
EPICS
Asyn Record Support
(asynRecord)
EPICS
AI Record Support
EPICS
AO Record Support
EPICS
BI Record Support
EPICS
BO Record Support
EPICS
MBBI Record Support
Octal IP-Module (tyGSOctal)
asynDriver
asynManager
portDriver
asynOctet

## Slide 7: Common record initialization scenario
EPICS
Record Support
Love
Device Support
Asyn
EPICS
Utilities
XX__init()
createAsynUser()
parseLink()
validateParams()
connectDevice()
findInterface()
lov__recordInit()

## Slide 8: Read AI record scenario
EPICS
Record Support
Love
Device Support
Asyn
Love
Interpose Interface
ai_read()
queueRequest()
callback()
preProcess()
executeCommand()
write()
process()
Love
Controller
write message
read()
read response
ai_read()
ioCompletion()
write
read

## Slide 9: loveApp standalone application
Sample application,
New with the release,
Supports vxWorks and Linux,
Database with PVs for each command,

## Slide 10: loveApp Initialization Scenario
Startup
Cmd File
Octal IP Module
Asyn Port Driver
Love Interpose
EPICS
Love Device Support
Init IP carrier
Init Serial Port
Load database
Init record inst.
Init Interpose Lovelink
Register record,device,driver
Load database records
Init IOC
Config Serial Port
Create device
Init IP module

## Slide 11: Reporting (dbior)
General
Information
Item
Number
Controller
Address
Controller
Model
Controller
Command
Record
Type
PV
Name
Asyn
Status
Access
Counter
Asyn
Port Name
PACT
State

## Slide 12: MEDM screens

## Slide 13: Distribution
Standard directories,
  Configuration,
    Requires Asyn 4-2 and Ipac 2-8,
  Documentation,
    Model 1600 and 16A,
    485LDRC RS232/RS485 converter,
    Release notes, known issues,
    Wiring diagram,
  Database, record instance files,
  iocBoot for Linux and vxWorks (startup scripts),
  MEDM displays,
Contains the sources,
  devAsynLove.c,
  interposeLovelink.c,
  devLove.cc,
  loveServer.cc,

## Slide 14: Improvements
Placement and usage of Asyn trace facility,
Usage of other Asyn interfaces,
Error reaction to communication timeout failure,
Further abstraction of record initialization methods,
???

## Slide 15: Acknowledgements
Marty Kraimer,
Ron Sluiter,

## Slide 16
Thank You
Code Inspections
Beamline Controls and Data Acquisition
APS Operations Division