## Slide 1: BCDA Cross Training
Love Controller Support
David Kline
April 4, 2005

## Slide 2: Contents
Overview,
Hardware Configurations,
Communication protocol,
Software Architecture,
  Common record initialization scenario,
  Read AI record scenario,
loveApp standalone application,
  Initialization scenario,
Reporting (dbior),
MEDM screens,
Distribution,
Improvements,
Acknowledgements,

## Slide 3: Overview
Love Controller,
  Instrument to measure voltage, current, thermocouple,
  Support models 1600 and 16A,
  Communication is through 2-wire RS485,
Device support,
  Old support based on MPF,
  New support based on Asyn,
  The echoServer and devMPC were departure points,
  Includes an interpose interface,
  Standalone application is available,
  IP-Octal RS232 and RS485 modules can be used,
Purpose of the new device support,
  Use as a learning tool for Asyn-based device support,
  Migrate from the unsupported MPF to Asyn,
  Appoint one as the owner of the module,
  Provide OS independence,

## Slide 4: Hardware Configuration – RS232 <-> RS485
Love
Controller
Model 16001
SBS XM-Octal-IO
Love
Controller
Model 16A2
Love
Controller
Model 1600n-1
Love
Controller
Model 1600n
B&B Electronics 485LDRC
Converter
B(+)
A(-)
RS485
RS232
TD
RD
MVME5100
SBS 626 (TVME200)
IP-OCTAL

## Slide 5: Hardware Configuration – RS485
MVME5100
Love
Controller
Model 16001
SBS XM-Octal-IO
Love
Controller
Model 16A2
Love
Controller
Model 1600n-1
Love
Controller
Model 1600n
B(+)
A(-)
SBS 626 (TVME200)
IP-OCTAL

## Slide 6: Communication
2-wire RS485,
Master/slave protocol, command, response messages,
Message format (simple),
  Sent and received as ASCII hex,
  Cmd:
    Read: <STX>L<ADDR><CMD><CS><ETX>
    Write: <STX>L<ADDR><CMD><VALUE><CS><ETX>
  Rsp:
    Data: <STX>L<ADDR><RSP><CS><ACK>
    Err: <STX>L<ADDR>N<CODE><ACK>
How does device support know commands?
  INP/OUT fields,
  field(INP,”@asyn(PORT,ADDR) CMD MODEL”)

## Slide 7: Software Architecture (coarse granularity)
Hardware Port
Lovelink Interpose Interface Layer (interposeLovelink)
Love Device Support (devAsynLove)
EPICS
Asyn Record Support
(asynRecord)
EPICS
AI Record Support
EPICS
AO Record Support
EPICS
BI Record Support
EPICS
BO Record Support
EPICS
MBBI Record Support
Octal IP-Module (tyGSOctal)
drvAsynSerialPort

## Slide 8: Software Architecture (fine granularity)
drvAsynSerialPort
asynCommon
asynOctet
asynOption
interposeEos
asynOctetBase
interposeLovelink
asynOctet
devAsynLove
MBBI
BO
BI
AO
AI
asyn Port “S0”
asyn Port “S0”

## Slide 9: Common record initialization scenario
EPICS
Record Support
Love
Device Support
Asyn
EPICS
Utilities
XX__init()
createAsynUser()
parseLink()
validateParams()
connectDevice()
findInterface()
lov__recordInit()

## Slide 10: Read AI record scenario
EPICS
Record Support
Love
Device Support
Asyn
Love
Interpose Interface
ai_read()
queueRequest()
callback()
preProcess()
executeCommand()
write()
process()
Love
Controller
write message
read()
read response
ai_read()
ioCompletion()

## Slide 11: loveApp standalone application
Sample application,
New with the release (R3-0-0),
Supports vxWorks and Linux,
Database with PVs for each command,

## Slide 12: loveApp Initialization Scenario
Startup
Cmd File
Octal IP Module
Asyn Port Driver
Love Interpose
EPICS
Love Device Support
Init IP carrier
Init Serial Port
Load database
Init record inst.
Init Interpose Lovelink
Register record,device,driver
Load database records
Init IOC
Config Serial Port
Create device
Init IP module

## Slide 13: Reporting (dbior)
General
Information
Item
Number
Controller
Address
Controller
Model
Controller
Command
Record
Type
PV
Name
Asyn
Status
Access
Counter
Asyn
Port Name
PACT
State

## Slide 14: MEDM screens

## Slide 15: Distribution
Standard directories,
  Configuration,
    Requires Asyn 4-2 and Ipac 2-8,
  Documentation,
    Controller and converter Information,
    Release notes, known issues,
    Wiring diagram,
  Database, record instance files,
  iocBoot for Linux and vxWorks (startup scripts),
  MEDM displays,
Contains the sources,
  devAsynLove.c,
  interposeLovelink.c,
  devLove.cc,
  loveServer.cc,

## Slide 16: Improvements
Current issues,
  Cannot easily debug an individual controller,
  Tight coupling between device support and model type (i.e. INP/OUT),
  Device support controls the command / response processing,
Solutions,
  Develop a multidevice driver,
  Employ different approach to reduce coupling,

## Slide 17: Improvements – Multidevice port driver
Develop a multidevice port driver,
Replaces the existing interposeLovelink layer,
Placed on top of drvAsynSerialPort,
Creates multiple connections to an Asyn port,
Allows connections to individual controllers,
Monitor individual controller communication,

## Slide 18: Improvements – Multidevice port driver
drvAsynSerialPort
asynCommon
asynOctet
asynOption
interposeEos
asynOctetBase
asyn Port “S0”
drvLove
asynOctet
asynOctetBase
asyn Port “L0”
devAsynLove
AI
“L0” addr=1
AO
addr=1
BI
addr=3
BO
addr=4
MBBI
addr=5
asynCommon

## Slide 19: Improvements – Different approach
Modify the information supplied to INP/OUT,
Employ the drvAsynSerialPort and drvLove drivers,
Implement an interpose at layer to,
  Define interfaces for the specific model (i.e. love1600),
  Provide a method to map the controller address to model type,
  Reduces the need for conditional statements,
  Introducing new model type is cleaner,

## Slide 20: Improvements – Different approach, cont…
drvAsynSerialPort
asynCommon
asynOctet
asynOption
interposeEos
asynOctetBase
asyn Port “S0”
asyn Port “L0”
devAsynLove
interposeLove
love1600
love16A
asynOption
AI
“L0” addr=1
AO
addr=1
BI
addr=3
BO
addr=4
MBBI
addr=5
asyn Port “L0”
drvLove
asynOctet
asynOctetBase
asynCommon

## Slide 21: Acknowledgements
Marty Kraimer,
Ron Sluiter,

## Slide 22: Observation
…it’s all about the interfaces and the methods that implement that interface…

## Slide 23
Thank You
Cross Training
Beamline Controls and Data Acquisition
APS Operations Division