## Slide 1: Next Generation CA Server
Jeff Hill

## Slide 2: Next Gen CA Server – Overview
LANSCE Requirements
  a Review
Server Design Fundamentals
  a Review
Demo
Data Access –
  a Review and Recent Changes
Status, benefits

## Slide 3: Next Gen CA Server – LANSCE Requirements
LANSCE timing and flavoring of data
  Flavoring
    Selection based on - logical combinatorial of beam gates
  Timing
    Selection based on - time sampling (single element) within a beam pulse
Many permutations
  Too many to, a-priori, install records for all of them
  Need LANSCE timing and flavoring specific subscription update filtering

## Slide 4: Next Gen CA Server – LANSCE Requirements
LANSCE timed data requires Array Index Metadata
  Magnitude of zero-eth element index
    Floating point
  Magnitude of one index increment
    Floating point
  Units of these magnitudes
    String

## Slide 5: Next Gen CA Server – Design Choices
  Channel Access client must
    specify LANSCE timing, flavoring needed when subscribing
  Channel Access service must
    tag the data with LANSCE timing, flavoring attributes
  Channel Access server must
    Appropriately filter subscription updates
  but …
  This must be done in a generic way to allow parallel capabilities at other EPICS installations
  Minimal to no impact on performance if the client does not request a filtered update stream
  Within the IOC, record processing must not be disturbed by filtering activities in the server

## Slide 6: Next Gen CA Server– Design Fundamentals
Event Queue – bridging the gap between two independent processing domains
  Service processing (i.e. Record processing)
    CPU Load is very predictable
    Deterministically scheduled, tightly synchronized to external events
    Must run at higher priority than the server components
  Client induced server load
    CPU Load is very unpredictable
    Non-deterministically scheduled, loosely synchronized to external events
    Must run in low priority components of the server

## Slide 7: Next Generation CA Server – Design Fundamentals
Event Queue – bridging the gap between two independent processing universes
  Clients read their input queues at very different rates
    Therefore each client attaching to the server must be serviced off of a private event queue
  Server production rate can exceed client consumption rate
    Buffering allows event sequences to be preserved over bursts of service activity
    Health of IOC requires that buffering capacity must be strictly limited
      During queue satuturation we have event replacement

## Slide 8: Demo
>camonitor fred
fred 2010-06-03 08:05:47.794268 16.4769
fred 2010-06-03 08:05:47.796998 10.3427
fred 2010-06-03 08:05:47.799992 15.7598

## Slide 9: Demo
>camonitor "fred$F $(PV:)>30 && $(PV)<40"
fred$F $(PV:)>30 && $(PV)<40 2010-06-03 07:58:47.224969 36.6466
fred$F $(PV:)>30 && $(PV)<40 2010-06-03 07:58:47.227964 37.1654
fred$F $(PV:)>30 && $(PV)<40 2010-06-03 07:58:47.267460 33.9427
fred$F $(PV:)>30 && $(PV)<40 2010-06-03 07:58:47.276013 33.9976
fred$F $(PV:)>30 && $(PV)<40 2010-06-03 07:58:47.299041 37.8033
fred$F $(PV:)>30 && $(PV)<40 2010-06-03 07:58:47.319065 33.549

## Slide 10: Demo
>camonitor "fred$F $(PV:flavor)==30 "
fred$F $(PV:flavor)==30 2010-06-03 07:58:18.906049 44.1145
fred$F $(PV:flavor)==30 2010-06-03 07:58:21.899019 39.2743
fred$F $(PV:flavor)==30 2010-06-03 07:58:24.885000 54.3352
fred$F $(PV:flavor)==30 2010-06-03 07:58:27.855063 93.9634
fred$F $(PV:flavor)==30 2010-06-03 07:58:30.811997 97.7081

## Slide 11: Next Generation CA Server – Data Access
Catalog, an introspection interface – implemented by data publisher
class CatalogTelesopeCoordinate : public Catalog { … };
void CatalogTelesopeCoordinate :: traverse ( Analyst & a ) const
{
publish ( a, pi_rightAscension, m_refTC.m_rightAscension );
publish ( a, pi_declination, m_refTC.m_declination );
}
Property Identifier
Property Value

## Slide 12: Next Generation CA Server – Data Access
Clerk a data querying and conversion interface– called by users
Clerk Library implements get
  Throws an exception if source datum is out of range in destination datum’s primitive type
Const Catalog & genericData;
Clerk clerk ( genericData );
Double rightAscension, declination;
clerk.get (pi_rightAscension, rightAscension );
clerk.get (pi_declination, declination );
Property Identifier
Property Value

## Slide 13: Data Access – Interface and Implementation are Independent
Déjà vu …
  To plug and play participants copy their data to GDD, CDevData, XxxData …
  Containers have inside a doubly linked list of fields
    Each field must be discriminated for scalar, vector, primitive type, bounds etc depending on how it will be used
      tagging or virtual base class storage overhead, every field
Data Access
  It is only a data introspection interface
    Storage formats remain compact and decoupled
      Data storage is typically the user’s flat data structure
  DA can wrap all of the above – the converse is not possible
  Introspector’s binding can be efficient
    Based on virtual functions – i.e. compile time binding

## Slide 14: Data Access – Efficiency Still Matters
Data Access enables transport of parasitic application specific data (such as the LANSCE flavor) through the system software layers while maintaining reasonable storage efficiency
  Data are polymorphic at the data structure level, and not at the field level. This implies better storage efficiency.
  Data are reference counted when they are stored in the event queues of multiple clients
  Same data payload can be used for multiple event types
  Nevertheless, we retain the ability to generically index the data during event filtering
  Data are allocated, and de-allocated, by the data producer
    Efficient free-lists based memory management is possible
Data on the event queue has good storage efficiency
  We actually do care about storage efficiency when buffering up multiple events on the event queue

## Slide 15: Data Access – Recent Changes
Now both types (Genus) and instances (Specimen) published from the same code – but one must use a template
typedef Index < Specimen > Catalog;
// Z: Genus, Specimen
template < class Z > class IndexAlarmLimits : public Index < Z > {};
template < class Z >
void IndexAlarmLowerLimits < Z > :: traverse ( Analyst & a ) const
{
publish ( a, pi_major, m_pDBR ->* pm_lower_alarm_limit );
publish ( a, pi_minor, m_pDBR ->* pm_lower_warning_limit );
}
Pointer to Member Data
Property Identifier
Pointer Class Specialized on Z

## Slide 16: Data Access – Recent Changes
Probe, the data inspector class
  Querying existence, type, bounds, etc
Const Cartalog & someData;
Probe probePV (someData, dbr :: pi_PV );
size_t count = probePV.elemCount ();
Size_t elemSize = probePV.elemSize ();
Probe :: Type type = probePV.type();
If ( type == Probe :: t_absent || type == Probe :: t_implicit ) { }
else if ( type == t_container ) {
}
Elis id ( type == t_integer ) {
}

## Slide 17: Next Generation CA Server – Process Variable Schema
pv {
timeStamp
alarm {
acknowledge { pending }
condition { status, severity }
}
limits {
display { upper, lower }
control { upper, lower }
alarm {
major { upper, lower }
minor { upper, lower }
}
}
labels
units
precision
  class { name }
  }
Green indicates that a value is stored. In a DA tree a node does not need to be a leaf node in order to carry a value. This allows for less hierarchy traversal when doing a basic fetch. For example.
Catalog & someData;
Clerk clerk (someData );
double value;
clerk.get (pi_pv, value );

## Slide 18: Next Generation CA Server – CA Response Payload Schema
success
PV schema (see previous slide)
other success schema depending on method invoked…
failure
context
unresponsive {…}
serviceDisconnect {…}
exceptionX {…}
exceptionY {…}
exceptionZ {...}
…
Context – character string containing complete context trace back to the source of the problem

## Slide 19: Next Gen CA Server – Status
Server is completed
  It runs, passes some of the tests, more testing in progress
Next step
  IOC integration

## Slide 20: Next Gen CA Server – Benefits for LANSCE
LANSCE style dynamic on-the-fly ad-hoc beam flavoring and beam timing experiments
  But, in homogenous EPICS system
Tool based approach to LANSCE applications
  Applications have abstract model of hardware
  Incremental upgrades hopefully easier
Multi-element “Timed” data
  COTS digitizer
  Window in time selected

## Slide 21: Next Gen CA Server – Benefits for EPICS Community
Flexible event snapshots
  Parameters other than alarm status, time stamp, scalar value correlated on event queue
  Array update bursts buffered on event queue
Subscription update filtering
  Expression (string) based means
    Project and site independent – tool based approach
    Minimally invasive for existing client side tools
Array index meta data
Expanding intersection of EPICS with data acquisition systems