## Slide 1: Diffcalc
Software for diffractometer control
Rob Walton
4th June 2010

## Slide 2: Introduction: GDA Epics Client
Diamond uses the open source GDA software (not SPEC)
  Paul Gibbons has introduced this here
  Client
    RCP (Eclipse) GUI
    Contains a Command line terminal
  ObjectServer
    Scannables and Detectors (Some Epics via JCA queue)
    Other handy things
Missing SPEC macros: fourc, sixc …
  Commands for diffractometer angle calculations
Substituting with Diffcalc
  Runs in the GDA’s ObjectServer’s Jython interpreter
Notes: Does not use SPEC – used by many other synchrotrons as command line user interface
We use GDA Software – Which Paul Gibbons has described at past meetings
Missing SPEC macros: fourc, sixc … used to calculate angles for diffractometers

## Slide 3: Overview
What does Diffcalc do? (Three theory slides)
Diffcalc
Diffcalc in the GDA

## Slide 4: 1) THEORY: Diffraction
Single crystals such as salt
  Made of many repeating unit-cells (cubes)
  X-rays at just the right wavelength and angle will diffract from planes of these cells
Braggs law

## Slide 5: Specifying a reflection
There are many (infinite) sets of planes
  Specify a set of with vector normal to their plane
  Miller indexes h, k, l (out of page)
h
k
0 1
1 0
1 2

## Slide 6: Diffractometers
Orient crystal and detector to look at reflections
4 circle
  Align to any h, k, l (3 circles)
  4th degree-of-freedom normally used to rotate about plane normal (Choose Mode)
5 and 6 circles
  Allow additional constraints (Choose Mode)
  reach hard-to-reach reflections
5 circle diffractometer
1
2
3
4
5
Notes: Also 5 and 6 circles allow either additional constraints, or to reach reflections that might not be reachable with a 4 circle.

## Slide 7: An experiment
With SPEC macros or Diffcalc:
Setup
  Specify shape of unit cell
  Find two reflections to infer crystal orientation on mount
Moving
  Read hkl position from circle angles
  Choose a mode
  Go to an hkl position

## Slide 8: 2) DIFFCALC
Written in Python
  Scientists can extend it themselves
  Thoroughly unit tested
Environment
  Standalone in Python
  GDA software’s Jython interpreter
Used on three beamlines. One more by end of year.
Implements papers:
  Busing & Levi (1966), "Angle Calculations for 3- and 4- Circle X-ray and Neutron Diffractometers", Acta Cryst. 22, 457
  Elias Vlieg & Martin Lohmeier (1993), "Angle Calculations for a Six-Circle Surface X-ray Diffractometer", J. Appl. Cryst. 26, 706-716
Based on and tested against existing software
  Elias Vlieg’s DIF software (closely)
  SPEC
  Alexander Bombardi’s software

## Slide 9: DiffractionCalculator object
UBCalculator - alignment
AngleCalculator for generic 6 circle case
  GeometryPlugin to customise
Passive only
  HwMonitorPlugin
Methods:
  setlat
  addref
  hklmode
  fixpar
  hklToAngles / AnglesToHkl
DiffractionCalculator
AngleCalculator
UBCalculator
AngleMapper
HWMonitorPlugin
GeometryPlugin

## Slide 10: Modes
> hklmode
Available modes:
0) fourc fixed-bandlw (alpha, blw)
1) fourc bisecting (alpha)
2) fourc incoming (alpha, betain)
3) fourc outgoing (alpha, betaout)
4) fourc azimuth (alpha, azimuth)
5) fourc fixed-phi (alpha, phi)
10) fivec bisecting ()
11) fivec incoming (betain)
12) fivec outgoing (betaout)
Current mode:
1) fourc bisecting
Current Parameters:
alpha: 0.0
gamma: 0.0 (fixed by diff.)
betain: --- (NA for mode)
betaout: --- (NA for mode)
azimuth: --- (NA for mode)
phi: --- (NA for mode)
blw: --- (NA for mode)

## Slide 11: 3) DIFFCALC IN THE GDA
DiffractionCalculator
(with ScannableMonitorPlugin)
hkl
h
k
l
hklverbose
alpha_par
betaout
betain
fivec
α
δ
ω
χ
φ
en
wl
Running in the GDA ObjectServer’s Jython Interpreter

## Slide 12: Commands/Demo
Methods exposed to user as commands:
> newub ‘demo’
> setlat ‘cubic’ 1 1 1 90 90 90
> pos wl 1
> pos fivec [0 60 30 1 0]
> addref 1 0 0
> pos chi 91
> addref 0 0 1
Calculating UB matrix.
> checkub
energy h k l h_c k_c l_c
1 12.3984 1.00 0.00 0.00 1.00 0.00 -0.0
2 12.3984 0.00 0.00 1.00 0.00 0.00 1.00
> def p(s):
> print s
> p(1)
1
Standard Jython terminal
> alias(‘p’)
> p 1
1
> p [1 2 3]
[1,2,3]
But…
‘Extended syntax’

## Slide 13: Moving and Scanning
> pos wl 1
> pos hkl [1 0 0]
> scan betain 1 3 .1 hkl [1 0 0] det 1
> scan en 1 10 1 hkl [1 0 0] det 1
> rscan h -.1 .1 .01 det 1
> scan hkl [1 0 0] [0 0 1] [ -.1 0 .1]
Use standard gda commands pos and scan
  Like any other Scannable (motor, detector etc.)
  E.g. :

## Slide 14: Conclusion
Open GDA and Diffcalc  SPEC (Disclaimer: Not all SPEC diffractometer macros are implemented)
Available at opengda.org with documentation
rob.walton@diamond.ac.uk