## Slide 1: Service-Oriented Architecture for High-level Applications
Paul Chu FRIB Controls Group Leader (Acting)

## Slide 2: Outline
What is Service-Oriented Architecture (SOA)
Why SOA needed
Services in consideration
Possible communication protocols
Summary

## Slide 3: What is SOA?
Service-oriented architecture (SOA) is a flexible set of design principles used during the phases of systems development and integration in computing. A system based on a SOA will package functionality as a suite of interoperable services that can be used within multiple, separate systems from several business domains.
-- Wikipedia
Everybody wants to be served, but not doing all the tedious work

## Slide 4: Why SOA Needed?
Reliability improvement
  Services are centrally controlled with rigorous requirements
  Each service focused on very few functions (Modularized services)
    Functionality distributed to various services – reduce complexity
  Without GUI overhead
Performance improvement
  Running on fast servers
  Data always available to clients
Applications are thin clients – easy to code
Only “narrow” APIs defined
  More portable
Service is not a new idea – been used for many years
SOA technology is transparent to clients – as long as APIs unchanged

## Slide 5: Services
Service-oriented architecture (SOA) example diagram

## Slide 6: High-Level Controls Architecture
Courtesy V. Vuppala

## Slide 7: Service Layer (V. Vuppala)
  Directory Service: Information about the control system including its services
  Device Service: Access and control of instruments (IOCs)
  Configuration Service: Physical and logical information about the accelerator and its component systems: magnets, RFQs, detectors, solenoids, power supplies, geographical location etc
  Lattice Service: Information about the accelerator lattice, that is the physical details about the optical elements
  Model Service: Service that simulates the accelerator or its sub-systems
  Log Book Service: To manage entries in the log book
  State: To save/restore state of the accelerator or its sub-systems
  Alarm Service: A service that provides access to alarm information (set changes, set/read mismatches, read alarms (e.g. temperatures or humidity that is too high, turbo pump currents, vacuum levels, etc.) and alarm configuration data.
  Authentication Service: Authenticates users, and authorizes access to services, devices, instrument access, etc.

## Slide 8: Service Example [1] (courtesy G. Shen)
A prototype of online model server service at NSLS-II
  Use PVData to store machine setting, simulation configuration, and in-memory simulation results
  Access the model server through PVAccess protocol
PVRecords (Model data & Setting)
Tracy
...
Presentation Client
Presentation Client
Support code
Model run control
Interface Adaptor
PVAccess
Elegant

## Slide 9: Service Example [2]
IRMIS E-log Service
  A Java or web-based service for IRMIS database access
  Database connection managed by service – no initial connection overhead
  Reduce the total number of connection requests to the database – all client traffic via the service
  No SQL knowledge required for application developers – all data access via API
  Business logic at service, not in database
IRMIS E-log Architecture
Courtesy E. Berryman

## Slide 10: Service Example [3]
Linac Energy Manager
  Constantly update the energy tracking information along the linac
  Magnetic fields can be scaled accordingly to maintain same lattice
  Run in an endless loop
  Update energies in the service
  “LEMLite” is to fudge klystron amplitude based on certain fixed energy reference points
    This can be an “RF Service” by itself
  At SLAC, currently using EPICS CA as the communication protocol

## Slide 11: Possible Communication Protocols
Different services may have different requirements
  E.g. data rate, data complexity, data amount…
EPICS (v.3) CA
EPICS (v.4) pvAccess
REST (Representational State Transfer)
SOAP (Simple Object Access Protocol)
JMS (Java Message Service)
XML-RPC
JSON-RPC
Web support is optional

## Slide 12: Summary
SOA is the way to go
A list of first order services identified
Several services been implemented/prototyped
Collaboration
  FRIB/MSU
  BNL/NSLS-II
  SLAC
  Everyone is welcome