## Slide 1: Cookbook
written by Gabriele Carcassi performed by Ralph Lange Oct 12 2011

## Slide 2: PVManager goals
Simplify data collection and aggregation
Simplify client development
Multiple sources (ca, pva, simulated, …)
Re-use code as much as possible
More than a client library, it’s a configurable client stack
Past talks went through the motivation and the architecture. This talk will go through some examples to showcase the power and the ease of use.

## Slide 3: The one architecture slide
Notifier
Collector
Monitor
Cache
PV Function
PV Function
Source rate
Desired rate

## Slide 4: Configuring data sources
// Sets CAJ (pure java implementation) as the default data source,
// monitoring both value and alarm changes
PVManager.setDefaultDataSource(new JCADataSource());

## Slide 5: Configuring data sources
// Sets CAJ (pure java implementation) as the default data source,
// monitoring both value and alarm changes
PVManager.setDefaultDataSource(new JCADataSource());
// For ultimate control, you can create the JCA context yourself
// and pass it to the data source
Context jcaContext = ...
PVManager.setDefaultDataSource(new JCADataSource(jcaContext, Monitor.VALUE | Monitor.ALARM));

## Slide 6: Configuring data sources
// Sets CAJ (pure java implementation) as the default data source,
// monitoring both value and alarm changes
PVManager.setDefaultDataSource(new JCADataSource());
// For ultimate control, you can create the JCA context yourself
// and pass it to the data source
Context jcaContext = ...
PVManager.setDefaultDataSource(new JCADataSource(jcaContext, Monitor.VALUE | Monitor.ALARM));
// Create a multiple data source, and add different data sources
CompositeDataSource composite = new CompositeDataSource();
composite.putDataSource("ca", new JCADataSource());
composite.putDataSource("sim", new SimulationDataSource());
// If no prefix is given to a channel, use JCA as default
composite.setDefaultDataSource("ca");
// Set the composite as the default
PVManager.setDefaultDataSource(composite);

## Slide 7: Configuring notifications
// For Swing applications, import from here
import static org.epics.pvmanager.util.Executors.*;
// Route notification for this pv on the Swing EDT
PVReader<?> pvReader = PVManager.read(...) .notifyOn(swingEDT()).every(ms(100));

## Slide 8: Configuring notifications
// For Swing applications, import from here
import static org.epics.pvmanager.util.Executors.*;
// Route notification for this pv on the Swing EDT
PVReader<?> pvReader = PVManager.read(...) .notifyOn(swingEDT()).every(ms(100));
// In CSS/SWT, import from here
import static org.csstudio.utility.pvmanager.ui.SWTUtil.*;
// Route notification for this pv on the SWT thread
PVReader<?> pvReader = PVManager.read(...) .notifyOn(swtThread()).every(ms(100));

## Slide 9: Configuring notifications
// For Swing applications, import from here
import static org.epics.pvmanager.util.Executors.*;
// Route notification for this pv on the Swing EDT
PVReader<?> pvReader = PVManager.read(...) .notifyOn(swingEDT()).every(ms(100));
// In CSS/SWT, import from here
import static org.csstudio.utility.pvmanager.ui.SWTUtil.*;
// Route notification for this pv on the SWT thread
PVReader<?> pvReader = PVManager.read(...) .notifyOn(swtThread()).every(ms(100));
// Or you can change the default PVManager.setDefaultNotificationExecutor(swingEDT()); // It accepts a standard java.util.concurrent.Executor

## Slide 10: Read a single channel
// Let's statically import so the code looks cleaner
import static org.epics.pvmanager.ExpressionLanguage.*;
import static org.epics.pvmanager.util.TimeDuration.*;

## Slide 11: Read a single channel
// Let's statically import so the code looks cleaner
import static org.epics.pvmanager.ExpressionLanguage.*;
import static org.epics.pvmanager.util.TimeDuration.*;
// Read channel "channelName" up to every 100 ms
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(100));

## Slide 12: Read a single channel
// Let's statically import so the code looks cleaner
import static org.epics.pvmanager.ExpressionLanguage.*;
import static org.epics.pvmanager.util.TimeDuration.*;
// Read channel "channelName" up to every 100 ms
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(100)); // Register for notifications
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// Do something with each value
Object newValue = pvReader.getValue();
System.out.println(newValue);
}
});

## Slide 13: Read a single channel
// Let's statically import so the code looks cleaner
import static org.epics.pvmanager.ExpressionLanguage.*;
import static org.epics.pvmanager.util.TimeDuration.*;
// Read channel "channelName" up to every 100 ms
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(100)); // Register for notifications
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// Do something with each value
Object newValue = pvReader.getValue();
System.out.println(newValue);
}
});
// Remember to close
pvReader.close();

## Slide 14: Read all values from single channel
// Read channel "channelName" up to every 100 ms, and get all
// the new values from the last notification.
final PVReader<List<Object>> pvReader = PVManager.read(newValuesOf(channel("channelName"))).every(ms(100));

## Slide 15: Read all values from single channel
// Read channel "channelName" up to every 100 ms, and get all
// the new values from the last notification.
final PVReader<List<Object>> pvReader = PVManager.read(newValuesOf(channel("channelName"))).every(ms(100));
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// Do something with each value
for (Object newValue : pvReader.getValue()) {
System.out.println(newValue);
}
}
});

## Slide 16: Read all values from single channel
// Read channel "channelName" up to every 100 ms, and get all
// the new values from the last notification.
final PVReader<List<Object>> pvReader = PVManager.read(newValuesOf(channel("channelName"))).every(ms(100));
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// Do something with each value
for (Object newValue : pvReader.getValue()) {
System.out.println(newValue);
}
}
});
// Remember to close
pvReader.close();

## Slide 17: Handling errors
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(100));
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// By default, read exceptions are made available
// on the reader itself.
// This will give you only the last exception, so if
// more then one exception was generated after the last read,
// some will be lost.
Exception ex = pvReader.lastException();
// Note that taking the exception, clears it
// so next call you'll get null.
if (pvReader.lastException() == null) {
// Always true
}
}
});

## Slide 18: Read “timeouts”
// If after 5 seconds no new value comes (i.e. pvReader.getValue() == null)
// then a timeout is sent. PVManager will _still_ try to connect,
// until pvReader.close() is called.
// The timeout will be notified only on the first connection.
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).timeout(sec(5)).every(ms(100));
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// Timeout are passed as exceptions. This allows you to
// treat them as any other error conditions.
Exception ex = pvReader.lastException();
if (ex instanceof TimeoutException) {
System.out.println("Didn't connected after 5 seconds");
}
}
});

## Slide 19: Read map with multiple channels
// Read a map with the channels named "one", "two" and "three"
final PVReader<Map<String, Object>> pvReader = PVManager.read(mapOf( latestValueOf(channels("one", "two", "three"))))
.every(ms(100));

## Slide 20: Read map with multiple channels
// Read a map with the channels named "one", "two" and "three"
final PVReader<Map<String, Object>> pvReader = PVManager.read(mapOf( latestValueOf(channels("one", "two", "three"))))
.every(ms(100));
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// Print the values if any
Map<String, Object> map = pvReader.getValue();
if (map != null) {
System.out.println("one: " + map.get("one") +
" - two: " + map.get("two") +
" - three: " + map.get("three"));
}
}
});

## Slide 21: Read map with multiple channels
// Read a map with the channels named "one", "two" and "three"
final PVReader<Map<String, Object>> pvReader = PVManager.read(mapOf( latestValueOf(channels("one", "two", "three"))))
.every(ms(100));
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// Print the values if any
Map<String, Object> map = pvReader.getValue();
if (map != null) {
System.out.println("one: " + map.get("one") +
" - two: " + map.get("two") +
" - three: " + map.get("three"));
}
}
});
// Remember to close
pvReader.close();
// Note that when using a composite datasource, the channels can be from // different sources (e.g. "sim://noise" and "ca://mypv").

## Slide 22: Alias for an expression
// Read a map with the channels "one", "two" and "three"
// reffered in the map as "setpoint", "readback" and "difference"
final PVReader<Map<String, Object>> pvReader = PVManager.read(mapOf( latestValueOf(channel("one").as("setpoint") .and(channel("two").as("readback")) .and(channel("three").as("difference"))))) .every(ms(100));

## Slide 23: Alias for an expression
// Read a map with the channels "one", "two" and "three"
// reffered in the map as "setpoint", "readback" and "difference"
final PVReader<Map<String, Object>> pvReader = PVManager.read(mapOf( latestValueOf(channel("one").as("setpoint") .and(channel("two").as("readback")) .and(channel("three").as("difference"))))) .every(ms(100));
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// Print the values if any
Map<String, Object> map = pvReader.getValue();
if (map != null) {
System.out.println("setpoint: " + map.get("setpoint") +
" - readback: " + map.get("readback") +
" - difference: " + map.get("difference"));
}
}
});

## Slide 24: Alias for an expression
// Read a map with the channels "one", "two" and "three"
// reffered in the map as "setpoint", "readback" and "difference"
final PVReader<Map<String, Object>> pvReader = PVManager.read(mapOf( latestValueOf(channel("one").as("setpoint") .and(channel("two").as("readback")) .and(channel("three").as("difference"))))) .every(ms(100));
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
// Print the values if any
Map<String, Object> map = pvReader.getValue();
if (map != null) {
System.out.println("setpoint: " + map.get("setpoint") +
" - readback: " + map.get("readback") +
" - difference: " + map.get("difference"));
}
}
});
// Remember to close
pvReader.close();

## Slide 25: Opening a vDouble channel
// Read a vDouble (which corresponds to a DBR Double)
// If the channel type does not match, exception is sent and no value is
// ever notified
final PVReader<VDouble> pvReader = PVManager.read(vDouble("currentRB")).every(ms(10));
pvReader.addPVReaderListener(new PVReaderListener() {
public void pvChanged() {
VDouble value = pv.getValue();
if (value != null) {
System.out.println(value.getValue() + " " + value.getAlarmSeverity());
}
}
});

## Slide 26: Converting types
// Conversions are explicit and work the same with different protocols. // Takes the value and tries to convert it to a vDouble if possible. // If not, the value is discarded.
final PVReader<VDouble> pvReader = PVManager.read(vDoubleOf(channel("count"))).every(ms(10));
// Takes the value and tries to convert it to a vDoubleArray if possible. // If not, the value is discarded.
final PVReader<VDoubleArray> pvReader = PVManager.read(vDoubleArrayOf(channel("intArray"))).every(ms(10));

## Slide 27: Using partial types
// Open a channel to handle all types
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(10));

## Slide 28: Using partial types
// Open a channel to handle all types
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(10));
pvReader.addPVReaderListener(new PVReaderListener() {
@Override
public void pvChanged() {
Object value = pvReader.getValue();
// We can extract the different aspect of the read object,
// so that we can work on them separately
}
});

## Slide 29: Using partial types
// Open a channel to handle all types
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(10));
pvReader.addPVReaderListener(new PVReaderListener() {
@Override
public void pvChanged() {
Object value = pvReader.getValue();
// This returns the interface implemented (VDouble, VInt, ...)
Class<?> type = ValueUtil.typeOf(value);
}
});

## Slide 30: Using partial types
// Open a channel to handle all types
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(10));
pvReader.addPVReaderListener(new PVReaderListener() {
@Override
public void pvChanged() {
Object value = pvReader.getValue();
// This returns the interface implemented (VDouble, VInt, ...)
Class<?> type = ValueUtil.typeOf(value);
// Extracts the alarm if present
Alarm alarm = ValueUtil.alarmOf(value);
}
});

## Slide 31: Using partial types
// Open a channel to handle all types
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(10));
pvReader.addPVReaderListener(new PVReaderListener() {
@Override
public void pvChanged() {
Object value = pvReader.getValue();
// This returns the interface implemented (VDouble, VInt, ...)
Class<?> type = ValueUtil.typeOf(value);
// Extracts the alarm if present
Alarm alarm = ValueUtil.alarmOf(value);
// Extracts the time if present
Time time = ValueUtil.timeOf(value);
}
});

## Slide 32: Using partial types
// Open a channel to handle all types
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(10));
pvReader.addPVReaderListener(new PVReaderListener() {
@Override
public void pvChanged() {
Object value = pvReader.getValue();
// This returns the interface implemented (VDouble, VInt, ...)
Class<?> type = ValueUtil.typeOf(value);
// Extracts the alarm if present
Alarm alarm = ValueUtil.alarmOf(value);
// Extracts the time if present
Time time = ValueUtil.timeOf(value);
// Extracts a numeric value if present
Double number = ValueUtil.numericValueOf(value);
}
});

## Slide 33: Using partial types
// Open a channel to handle all types
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(10));
pvReader.addPVReaderListener(new PVReaderListener() {
@Override
public void pvChanged() {
Object value = pvReader.getValue();
// This returns the interface implemented (VDouble, VInt, ...)
Class<?> type = ValueUtil.typeOf(value);
// Extracts the alarm if present
Alarm alarm = ValueUtil.alarmOf(value);
// Extracts the time if present
Time time = ValueUtil.timeOf(value);
// Extracts a numeric value if present
Double number = ValueUtil.numericValueOf(value);
// Extract display information if present
Display display = ValueUtil.displayOf(value);
}
});

## Slide 34: Using partial types
// Open a channel to handle all types
final PVReader<Object> pvReader = PVManager.read(channel("channelName")).every(ms(10));
pvReader.addPVReaderListener(new PVReaderListener() {
@Override
public void pvChanged() {
Object value = pvReader.getValue();
// This returns the interface implemented (VDouble, VInt, ...)
Class<?> type = ValueUtil.typeOf(value);
// Extracts the alarm if present
Alarm alarm = ValueUtil.alarmOf(value);
// Extracts the time if present
Time time = ValueUtil.timeOf(value);
// Extracts a numeric value if present
Double number = ValueUtil.numericValueOf(value);
// Extract display information if present
Display display = ValueUtil.displayOf(value);
displayAlarm(alarm);
displayTime(time);
...
}
});

## Slide 35: Aggregating a vTable
// Create a table with 2 columns, pv name and value, and 3 rows List<String> names = Arrays.asList("one", "two", "trhee");
final PVReader<VTable> pvReader = PVManager.read(vTable(
column("Names", vStringConstants(names)),
column("Values", latestValueOf(channels(names)))))
.every(ms(100));

## Slide 36: Aggregating a vTable
// Create a table with 2 columns, pv name and value, and 3 rows List<String> names = Arrays.asList("one", "two", "trhee");
final PVReader<VTable> pvReader = PVManager.read(vTable(
column("Names", vStringConstants(names)),
column("Values", latestValueOf(channels(names)))))
.every(ms(100));
pvReader.addPVReaderListener(new PVReaderListener() {
@Override
public void pvChanged() {
VTable vTable = pvReader.getValue();
// First column is the names
String[] names = (String[]) vTable.getColumnArray(0);
// Second column is the values
double[] values = (double[]) vTable.getColumnArray(1);
// ...
}
});

## Slide 37: Underlying concept
Every choice is explicit. You decide:
  which types you expect something to be and whether you want a standard conversion
  whether you want a queue of all values, or a cache with the last one
  what maximum rate you’ll get notifications
Some choices are mandatory
  You are forced to decide the above, or you won’t have a client that degrades gracefully
Simple choices are simple, complicated possible
The power is in the combinatory of the operators

## Slide 38: Some numbers (Bob likes numbers)
42
1
e
p
2
13.999

## Slide 39: Some performance numbers
Latency from first request to first received data
  direct CAJ: 13.57 +/- 2.02 ms
  pvManager 5 ms scan: 17.90 +/- 1.62 ms
3493 channel requests to all received data
  direct CAJ 9.6 sec cold 2.5 sec warm
  pvManager (separate): 13.4 sec cold 2.5 sec warm
  pvManager (single list): 10.7 sec cold 2.5 sec warm

## Slide 40: Performance video
Watch for:
  Rate throttling: notification rate decreases automatically if client can’t keep up
  Rate limit: notification rate is limited (25Hz for Probe, 50Hz for plot – more is useless)
You can’t write a pvManager app that does not rate limit and throttle!