## Slide 1: Extensions to the Asyn Driver for Data Acquisition
Klemen Zagar <klemen.zagar@cosylab.com>
May 2nd, 2013

## Slide 2: Outline
Motivation
Architecture
Data acquisition functionality
Other uses
  Image acquisition
  Signal generation
  Timing receivers
Status & roadmap

## Slide 3: Motivation
Data acquisition devices have a lot in common:
  Acquire a sample/waveform.
  Sampling rate.
  Triggering conditions.
  Unit conversion…
ITER diagnostics: Could the interface for accessing and configuring common functionality be somehow standardized?
  At level of EPICS PVs?
Benefits:
  Write “high-level” applications and interchange DAQ devices.
  Operate DAQ devices in the same way (reset, firmware update, trigger configuration, …)
  Specify functionality by ticking what needs to be supported, rather than writing a spec for every DAQ device.
  Reusable automated tests.

## Slide 4: The idea is by no means new…
EPICS base already pre-defines a very useful collection of records (ai, ao, mbbi, …, motor record).
Generic Transient Recorder (GTR):
  http://www.aps.anl.gov/epics/modules/analog/gtr/
  Clock, trigger (incl. pre-trigger and soft trigger), multiple events, number of samples.
  MEDM screen.
AreaDetector:
  http://cars9.uchicago.edu/software/epics/areaDetector.html
  Settings, image, image processing plugins

## Slide 5: NDS architecture
Nominal Device Support (NDS)
  A C++ “base class” from which device-specific drivers are to be derived
  Templates
    makeBaseApp.pl
    EPICS database
    Example device driver
  Documentation
    User’s manual
    Test plan
Based on the C++ asynPortDriver

## Slide 6: Documentation (user’s manual)

## Slide 7: Documentation (test plan)

## Slide 8: NDS classes
These are base classes, likely to be extended/overriden by device-specific driver

## Slide 9: NDS state machines
Device-level state machine:
Channel-level state machine:

## Slide 10: Implementing a device-specific driver
The EPICS DB template declares a record:
  For standard functions, the template defaults are used.
  Device-specific drivers are free to
    add records,
    or remove the ones that are not supported/applicable.
Register the read and/or write handlers, retrieve “callback interrupt ID”:
  For standard functions, done in the NDS base class.
  A single-liner to add custom functions.

## Slide 11: Implementing a device-specific driver
Implement the handler (called when record is processed):
  For many standard functions, already implemented in the base class (software emulation).
Dispatching interrupts (triggering record processing):

## Slide 12: Implementing a device-specific driver
“Message” mechanism:
Registering message handler
Registering state transition handlers

## Slide 13: DAQ functions
A superset of all one could think of…
Device-specific driver need not implement all…
  …but if it does, it would automatically comply with the “standard”.

## Slide 14: DAQ functions
General:
  Device information
  Device/channel state
  Executing self-tests
  Firmware update (including checksum & compatibility checks)
Clock settings
  Sample rate
  Clock multiplier
  Clock source
Triggering
  Trigger condition (including “soft trigger” – “now”)
  Trigger delay (negative – pre-trigger)

## Slide 15: DAQ functions
Filtering (FIR, IIR)
Unit conversion
  Piece-wise cubic splines
  Settable at run-time (double waveforms)
Signal generation
  Piece-wise cubic splines
  Sine, wave, pulse, ….
Fourier transforms
Streaming

## Slide 16: Timing devices
Logical “events”
  Something that happens on some timing device’s terminal
  Function-oriented
  Timestamped by the timing board
  Standardized way to control event timings (origin, delay, width, duty cycle, end time)

## Slide 17: Imaging devices
Similar to Area Detector...
  Advice: If in doubt, use Area Detector
Can use Area Detector plugins
Advantage of NDS imaging devices:
  NDS devices can talk directy with each other
  E.g., high-performance streaming of images timestamped with a NDS timing device

## Slide 18: Status & Roadmap
NDS 2.2 was released in April
  Support for timing devices
Currently used only by ITER diagnostics
Considering to be used for ESS
  Struck 8300 DAQ
  MRF-based event receiver
E-mail support process in place
Roadmap:
  Software support for FFT
  Automated tests
  Support for threading (lifecycle management, real-time settings, synchronization, timers, file descriptor polling, …)
  CSS screen

## Slide 19: Boards (planned to be) supported
Board | Developer
ADC12500 | RF-DA (ITER)
Struck SIS8300 (MTCA.4) | ATOS, Alceli (ITER, ESS, DESY)
TEWS TAMC641 | DMCS (ITER)
NI PXI-6682 and NI PXI-6683 | NI (ITER)
PTM-DAMC-1588-10 (MTCA.4 timing) | ITER, DMCS (ITER)
ATX-AMC-PTP (ATCA timing) | ITER, IPFN (ITER)
ATCA-IO-PROCESSOR (32-channel DAQ) | IPFN (ITER)
ADQ412-3G (MTCA.4 and PXIe, 4 channel 1.8GS/s ADC) | IPFN (ITER)
Microresearch Finland Timing Receiver | Cosylab (ESS)

## Slide 20: Interested?
Got a DAQ device to support?
  We can give:
    sources & docs
    offer support
    guidance / design advice
    and also implementation & QA
  Send e-mail to klemen.zagar@cosylab.com.
Use cases welcome, too!

## Slide 21: Thank you