## Slide 1: Acquisition of Long Waveform using Yokogawa SL1000
Shuei YAMADA
KEK / J-PARC
Notes: May 02, 16:30 10min + 5min

## Slide 2: Contents
J-PARC
Long-waveforms in J-PARC MR
Yokogawa SL-1000
Summary

## Slide 3: Japan Proton Accelerator Research Complex : J-PARC
Tokai village, Ibaraki 130km from Tokyo 80km from Tsukuba
Tokyo
Tsukuba
Notes: 130km away from tokyo

## Slide 4: J-PARC Facilities
©google
Hadron Experiment Facility
LINAC 180MeV/c 25Hz
RCS 3GeV/c 25Hz
Main Ring 30GeV/c 2.48 sec (FX) 6.0 sec (SX) In operation since 2008
Materials and Life Science Facility
Neutrino Experiment Facility
Pacific ocean
N
Notes: An aerial photo of J-PARC

## Slide 5: J-PARC Main Ring
©google
MW-class High Power Proton Synchrotron for Particle Physics and Hadron Physics
  T2K neutrino oscillation experiment
  Hadron experiments (e.g. Kaon rare decays)
  Future experiments (e.g. m-e conversion)
Slow-Cycle Machine
  Accelerate from 3 GeV to 30 GeV
  Fast Extraction 2.48 s [0.12 (inj) + 1.4 (acc) + recovery]
  Slow Extraction: 6.0 s [0.12 (inj) + 1.9 (acc) + 2.9 (sx) + recovery]
Need to monitor entire cycle, in cycle-by-cycle
 Long Waveforms are Important
Notes: An aerial photo of J-PARC

## Slide 6: Example of a Long Waveform: MR Beam Intensity
Record each cycle
  Requirements from Machine Operation
Estimators of Beam Loss, Slow Extraction quality
5sec @ 100kHz for waveform
1sec for data transfer
MR cycle (6 sec, Slow Extraction)
Notes: 2013.Sep 受注終了

## Slide 7: Yokogawa WE7000
30-40 Units being used in J-PARC MR
  DCCT, BPM, Magnet Power Supplies, etc.
  Many experiences
15 years old
  Small memory size: few MWords (depends on A/D module)
  Slow data transfer: 1800 kB/s (WE7000  EPICS IOC)
Discontinued
Notes: Data size: 3.64s * 100kHz * 2bytes/ch * 2 = 1456000 bytes = 1421.875 kB
1421.875 kB / 1.6s (UDP 1.4kbytes packet) 890 kB/s
1421.875 kB / 0.765s (UDP 32kbytes packet) 1860 kB/s
1998年に登場

## Slide 8: Yokogawa SL1000
Modular-type DAQ system
Replacement of WE7000
16 channels (2ch * 8slots)
Isolated inputs (850V)
Various A/D modules (100MHz12bit - 100kHz16bit)
Data transfer rate: 5900 kB/s (SL1000  IOC, preliminary)
Max. record length: 100MW/unit
VXI-11 (1000Base-T) & USBTMC
EPICS Device Support
Notes: 5 sec * 10kHz * 6ch * 2bytes / 1024 = 590 kBytes
590 kB / 0.1s = 5900 kB/s

## Slide 9: SL1000 Device Support
Yokogawa’s reference Implementation
  Oscilloscope (# of samples: 1-2-5 sequence)
  Decimated waveform per channel
  Single raw waveform record shared by all channels
KEK / J-PARC in-house ver.
  Based on Yokogawa’s
  Arbitrary number of samples
  Raw waveform per channel
  Testing in SX operation
http://www-linac.kek.jp/cont/epics/sl1000/

## Slide 10: Summary
 | WE7000 | SL1000
 | Modular-type DAQ system | Modular-type DAQ system
Life | 1997-2013 (discontinued) | 2007Dec-
EPICS Device Support | By KEK (2002-2012) | By Yokogawa (oscilloscope, db + OPI) By KEK (2012-, in J-PARC)
Data transfer rate | 1800 kB/s | 5900 kB/s (preliminary)
# of units in use | J-PARC MR 30-40 J-PARC LI …10 | Few (in test phase)

## Slide 11
Notes: 11

## Slide 13: MR Operation Modes
Fast Extraction
Slow Extraction

## Slide 14: Data Size in J-PARC MR : 400GB/week
Operation of MR and data taking started in 2008
MR cycle : 3 sec (FX), 6 sec (SX)
Record all waveform data each cycle
  As many waveform as possible
    3-50BT BPM
    MR Injection Error Monitor
    MR BPM
    MR DCCT
    SX Spill
Notes: 400GB / w = 2.4GB/day

## Slide 15: ROOT in J-PARC MR
ROOT-based
data acquisition tool : cadump
  Collects data from EPICS-records each MR cycle
  Save as ROOT-file
ROOT-file
  Self describing
  - Definition of data classes written in file
  Backward and forward compatible
  - Files created in 2010 should be readable in 2020
Data analysis using ROOT
storage
EPICS record
trigger
Offline Analysis
Online Monitor
cadump
EPICS record
EPICS record
ROOT-file