## Slide 1: EPICS for Experiments

## Slide 2: Programme
09:30: Introduction to EPICS (Nick Rees)
09:45: Asyn (Jon Thompson)
  C++, extending AsynPortDriver base class
  Parameters, threads, connecting to the device
10:45: Coffee Break
11:15: Motion (Jon Thompson)
  C++, extending the asyn motor base classes
  Compound motion
  Trajectory scanning
12:30: Lunch
13:15: Tours
14:30: Coffee Break
15:00: 2D Detectors (Tom Cobb)
  AreaDetector
    Standard plug-ins
    Data flow and attaching Meta-data
    C++, extending the area detector base classes

## Slide 3: What is EPICS?
A Collaboration
  A world wide collaboration that shares designs, software tools, and expertise for implementing large-scale control systems
A Control System Architecture
  A client/server model with an efficient communication protocol (Channel Access) for passing data
  A distributed real-time database of machine values
A Software Toolkit
  A collection of software tools collaboratively developed which can be integrated to provide a comprehensive and scalable control system

## Slide 4: Ten Great Things About EPICS
It is free.
It is Open Source
There are lots of users.
All you need to know to access data is a PV name.
You can pick the best tools out there ...
... or build your own.
The boring stuff is already done.
There is a lot of expertise available.
A good contribution becomes internationally known.
It doesn't matter whether you need 10 PVs or 10 Million PVs. It scales

## Slide 5: EPICS and Experiments
Where do you start?
  Download and build EPICS
    http://www.aps.anl.gov/epics/base/index.php
    Don’t forget to read the manual!
  Download and build some clients
    http://www.aps.anl.gov/epics/extensions/index.php
  Download and build some synApps support modules
    http://www.aps.anl.gov/bcda/synApps/index.php
  And don’t hesitate to ask the mailing list if you have problems
    http://www.aps.anl.gov/epics/tech-talk/index.php

## Slide 6: synApps
areaDetector
  Support for area (i.e., 2-D, or image) detectors, including CCDs, pixel array detectors, and online imaging plates. This module replaces the ccd and pilatus modules.
autosave
  Support for saving software parameters at run time, and restoring them during the next reboot. Autosave is also a way to initialize array PV's at boot time.
busy
  The busy record, which allows developers more ways to indicate when an operation is complete. Previously, this record was provided by the sscan module, because the sscan record is one of its beneficiaries.
calc
  Run-time expression evaluation, derived from the calcout record in EPICS base, and extended to operate on strings, arrays, and to implement coupled expressions.
camac
  Support for CAMAC hardware.
dac128V
  Support for an IndustryPack DAC module.
delaygen
  Support for delay generators, including the SRS DG645, Colby Instruments PDL100A, and Gigabaudics PADL3.
dxp
  Support for X-Ray Instrumentation Associates's DXP digital signal processor
ebrick
  Support and sample application for low-cost PC-104 and uCDIMM based IOC.
ip
  Support for various serial, and other message-based, devices.
ip330
  Support for an IndustryPack ADC module

## Slide 7: synApps
ipUnidig
  Support for an IndustryPack digital I/O module
love
  Support for Love controllers
mca
  Support for multichannel analyzers and multichannel scalers.
modbus
  Support for ModBus-protocol devices over TCP, serial RTU, and serial ASCII links
motor
  Support for motors
optics
  Support for optical tables, monochromators, slits, etc.
quadEM
  Support for an APS-developed 4-channel electrometer
softGlue
  Support for user-programmed "wiring" of custom FPGA content loaded into an Acromag IP-EP201 module.
sscan
  Support for scans (programmed control and data acquisition).
std
  Miscellaneous EPICS support, including the epid (extended PID), scaler, sseq (string sequence), and timestamp records; and pvHistory support.
stream
  Dirk Zimoch's streamDevice, in a module-flavored wrapper.

## Slide 8: synApps
utils
  Miscellaneous tools, including support for converting an application from one version of synApps to another; support for the MDA file format, written by the sscan module; and support for EPICS-application prototyping.
vac
  Support for vacuum controllers
vme
  Support for VME hardware
xxx
  Sample user-application directory
allenBradley
  for communicating with Allen Bradley PLC's (ANL)
ipac
  required for IndustryPack support (ANL)
asyn
  required by many modules (ANL)
seq
  for SNL programs in synApps (BESSY)
stream
  configurable device support for message-based devices (PSI)
devIocStats
  IOC statistics, replaces vxStats (SLAC)

## Slide 9: EPICS and Experiments
PV’s are fine, but how do you:
  Program a command/response object method paradigm when all EPICS can do is get/set and publish/subscribe simple primitive PV’s?
  Work with structured data when all you have is primitive types?
  Provide all the real-time stateful control that modern complex experimental instrumentation requires?
  Provide an interface for an inexperienced scientist when all you have all these busy engineering screens?

## Slide 10: EPICS completion reporting
Use only PP links and forward links in an execution chain.
SCAN
PUT_CALLBACK LINK
PP LINK
“BUSY”
“DONE”

## Slide 11: Structured Data
Lack of structured data is a weakness
However there are ways around it:
  Deal with it in the device driver (areaDetector)
  Sequential, ordered processing (monitoring for key events and sampling wider state).
  Other protocols.
  Deal with it principally in higher level applications.
It doesn’t seem to be a fundamental stumbling block.
EPICS v4 is designed to address it.
In many circumstances the simple data model is a major strength.
  At least you don’t have endless arguments about Normative data types...

## Slide 12: Scientific Interface
GDA Clients
GDA Server
EPICS Clients
Data Analysis
EPICS IOCs

## Slide 13: In Summary
EPICS is a paradigm shift for many software engineers
However, EPICS is a mature, robust and reliable framework that is flexible enough for most software/hardware interfacing issues.
The EPICS user community is a major strength.
  Someone, somewhere, has done something similar before.
EPICS is flexible enough to be used universally.
EPICS cannot do everything. You nearly always need something more for a scientific user interface.
  Call this an EPICS client, or call it <your favourite experiment control system>, but it provides the rich science interface.