## Slide 1: Building areaDetector against Debian
VS from source

## Slide 2: Building AreaDetector against Debian packages
NSLS2 is using Debian distribution
We have very recently upgraded NSLS2 distribution from epicsdeb.
In February 2018 Mark Rivers modified the areaDetector build infrastructure to allow areaDetector to be built against Debian EPICS deployment with selected packages built from source.
New .opi screens are converted by Mark Rivers and are available now in github in /autoconvert/
Kay Kazemir have been improving .adl -> .opi translator, addressing misc. translation problems. We believe it is close to perfect now.

## Slide 3: areaDetector built against Debian (1)
Maximally reuse community efforts, i.e. st.cmd to run the Prosilica IOC
        # Load all other plugins using commonPlugins.cmd
        < $(ADCORE)/iocBoot/commonPlugins.cmd
        set_requestfile_path("$(ADPROSILICA)/prosilicaApp/Db")
The commonPlugins.cmd load .db of the dependent modules
        # Optional: load scan records
        dbLoadRecords("$(SSCAN)/sscanApp/Db/scan.db", "P=$(PREFIX),MAXPTS1=2000,MAXPTS2=200,MAXPTS3=20,MAXPTS4=10,MAXPTSH=10")
        set_requestfile_path("$(SSCAN)/sscanApp/Db")
        # Optional: load sseq record for acquisition sequence
        dbLoadRecords("$(CALC)/calcApp/Db/sseqRecord.db", "P=$(PREFIX), S=AcquireSequence")
        set_requestfile_path("$(CALC)/calcApp/Db")
        # Optional: load devIocStats records (requires DEVIOCSTATS module)
        dbLoadRecords("$(DEVIOCSTATS)/db/iocAdminSoft.db", "IOC=$(PREFIX)")

## Slide 4: areaDetector built against Debian (2)
      oksana@xf28id1-ioc2:~$ locate scan.db
      /usr/lib/epics/dbd/menuSscan.dbd
      /usr/lib/epics/dbd/sscan.dbd
      oksana@xf28id1-ioc2:~$
      oksana@xf28id1-ioc2:~$ locate sseqRecord.db
      /usr/lib/epics/dbd/sseqRecord.dbd
      oksana@xf28id1-ioc2:~$
      oksana@xf28id1-ioc2:~$ locate iocAdminSoft.db
      /usr/lib/epics/db/iocAdminSoft.db
      oksana@xf28id1-ioc2:~$
In the debianized modules only files in
      module/db/
      module/dbd/
making to /usr/lib/epics/

## Slide 5: Discovered benefits from building areaDetector from source
Allows reusing st.cmd file with minimal changes.
    dbLoadRecords("$(SSCAN)/sscanApp/Db/scan.db“, …) dbLoadRecords("$(CALC)/calcApp/Db/sseqRecord.db“,…)
Can use latest EPICS7 base
Can easily port to Debian 7/ CentOS
Can have more upgrade freedom with
    AreaDetector and asyn being released ~ every 6 month.