## Slide 1: Odin Detector DAQ Framework and areaDetector Integration
EPICS areaDetector Working Group Meeting
APS, June 2018
Ulrik Pedersen
Head of Beamline Controls

## Slide 2: Odin
“Control and data acquisition framework
for parallel detector systems”
DLS – STFC Collaboration
Started: Late 2014

## Slide 3
Logo
Collaborators
GitHub
Cryptic Name
odin-detector

## Slide 4: Odin Detectors
In-house or collaborative detector development
  Different hats: detector system vendor & system integrators
Collaboration agreement: control system agnostic
Scalable, but simple to control
  Modular detector systems, multiple readout channels
  Single point of control of distributed system
DAQ system, not a processing pipeline
  But … descrambling pixels *is* processing

## Slide 5: Odin Detectors
Eiger…
Excalibur
Tristan
Percival

## Slide 6
Special Access
OdinControl
Python HTTP control server
Control
Odin
Control and data acquisition framework for parallel detector systems
ZMQ JSON
FrameReceiver
Data stream gatherer
FrameProcessor
Data processor and file writer
OdinData
C++ data acquisition and file writing stack

## Slide 7
C++ data acquisition and file writing stack
Excalibur
ZMQ JSON
OdinData
C++ data acquisition and file writing stack
ADOdin
Thin AreaDetector wrapper API
OdinControl
Python HTTP control server
RESTful API
TCP
Tristan
Percival
Control
Data

## Slide 8
C++ data acquisition and file writing stack
ZMQ JSON
Custom Python Client
Eiger X 4M
ADEiger
AreaDetector for detector control
RESTful API
OdinData
C++ data acquisition and file writing stack
Control
Data

## Slide 9: OdinControl
Generic HTTP server
Adapters provide functionality for each device
Server generates RESTful API from arbitrary Adapter attributes and methods
Control through simple webpages or client app

## Slide 10: OdinControl Server Configuration
Configure
server address
Load Adapter libraries
Configure
specific Adapters

## Slide 11: OdinData
FrameReceiver gathers data from UDP or ZeroMQ stream
Decoder plugin validates data packets and constructs a single frame
Passes data frame to FrameProcessor through shared memory

## Slide 12: OdinData
FrameProcessor receives message with frame pointer
Process plugin performs relevant processing to produce an image
  Descrambling detector specific data
Detector agnostic FileWriterPlugin writes pre-chunked data directly to HDF5 dataset
Notes:   Excalibur rotates sections and interpolates physical gaps
  Dimensions, data type and compression configured by client control

## Slide 13: OdinData
Write data using Direct Chunk Write
Only the raw dataset for best performance
A single, live, view of the data produced using Virtual Dataset and SWMR functionality
Notes:   Less processing and handles pre-compressed data
  Metadata is published on a ZeroMQ stream

## Slide 14: OdinData
Handle errors gracefully throughout
  Missing packets
  Missing full frames
Random ordering
  Frames stored in correct order in HDF5
Notes:   Less processing and handles pre-compressed data
  Metadata is published on a ZeroMQ stream

## Slide 15: areaDetector Integration - ADOdin
Beamlines require areaDetector
  Integration through GDA and/or Malcolm for scanning
Utilize the public HTTP/REST API
  Just like any other control system from our collaborators
Same idea as ADEiger and ADPilatus
  Control and status monitoring
  External servers/processes handle data stream

## Slide 16: areaDetector Integration - ADOdin
OdinData Configuration
Advanced HDF5 Configuration
OdinData Status (One for each process)
Notes: Thin AreaDetector API as a client to an OdinServer
Integrates the Odin framework within the EPICS control system
Provides familiar API to both controls engineers and GDA

## Slide 17: Excalibur
Notes: Excalibur is parallel by design
  Firmware fans frames out to each OdinData process round-robin

## Slide 18: VMXi Eiger X 4M
Notes: Eiger requires separate fan-out process to emulate the parallel Odin structure
  Necessary to cope with high frame rate (up to 750Hz)

## Slide 19: In Summary…
Odin is a control system agnostic single point of control
Integrates with areaDetector for beamline application
WIP but used on 2 detector systems
  Excalibur
  Eiger 4M
Odin is our Detector Control & DAQ backend for in-house and collaborative detector systems

## Slide 20: Thanks
Questions?
Gary Yendell (Diamond)
Tim Nicholls (STFC)
Alan Greer (Observatory Sciences/Diamond)
Matthew Taylor (Diamond)