## Slide 1: areaDetector at Diamond
Reporting use and recent developments at DLS
EPICS/areaDetector developers meeting
APS, June 2018
Ulrik Pedersen
Head of Beamline Controls

## Slide 2: areaDetectors at DLS
GigE cameras using aravisGigE
Pilatus
Eiger
PCO
Andor
XMAP
electronAnalysers
dtaq ADCs

## Slide 3: DLS in-house developments and collaborations
Excalibur
Percival
Merlin
Xspress
PanDaBox
  Not really an areaDetector but with an areaDetector driver!

## Slide 4: DLS Environment
RHEL6
  EPICS Base R3.14.12.3
  areaDetector 1-9 (!)
    But it just works…
  ADCore
    2-2, 2-3, 2-4, 2-6
RHEL7 (transitioning)
  EPICS Base R3.14.12.7
    .. Followed by EPICS 7
  ADCore 2-6
    .. Followed by 3-x

## Slide 5: HDF5 SWMR
Single Writer Multiple Reader
Process data while it is being written to file
HDF5 File
Writer
Reader
…that can be read by a reader…
with no IPC necessary.
New data elements…
… are added to a dataset in the file…

## Slide 6: areaDetector NDFileHDF5
Now with SWMR support
  Only available with HDF5 >= 1.10
  Optional enable/disable
  SWMR only works on POSIX file systems – not NFS/Samba/CIFS
Multiple dimensions in addition to the 2+1D
  Arrange data by scan dimension

## Slide 7: Mapping Project
Basic ‘mapping’ is simple: 2D raster-scan
Add multiple dimensions
Non-linear scans
Performance using hardware triggers
  Continuous scans
  Zebra or Panda
Live viewing through HDF5 files
  Images, spectra
Live processing of HDF5 files
  Pipelines triggered on scan start
1 mm
Abs
DPC
DF
C
O
C
O
Fe

## Slide 8: Mapping Project

## Slide 9: Mapping Project
HDF5 SWMR
GDA/DAWN visualisation
GDA Mapping Client
GDA9 Scanning
EPICS/ Malcolm Middleware
DAWN Processing
Messaging
Data

## Slide 10: Mapping Project

## Slide 11
HDF5 file
Other plugins here
Detector Driver
Position Labelling Plugin
Snake scan
Write data in snake pattern
Leave gaps for dropped frames
Rewind and overwrite data
Monitor HDF5 for live updates
HDF Writing Plugin
NDArray
XML
positions
XML
layout
NDArray
X:0 Y:0
X:1 Y:0
Position Plugin

## Slide 12
Even faster detectors…
Increased use of beamtime == larger datasets
Compression?
  Blosc filter already on HDF5 file writer (Xiaoqiang Wang, PSI)
  NDArray support for compressed frames?
New ways of storing and processing?
  Object Storage – S3 File Writer plugin?
  Streaming to in-house or external cloud?
Future