## Slide 1: Embedded Event Receiver at PSI
Roger Biffiger :: Software Engineer :: Paul Scherrer Institut
180612 :: EPICS collaboration meeting :: Open Hardware Workshop

## Slide 2: PSI – large research facilities has a new structure
PSI
      Large Research Facilities
          Electronics and Control Systems
              Digital Signal Processing
                FPGA development
                Embedded Software

## Slide 3: SwissFEL
1st phase 2013-16
2nd phase 2018-19?
Linac 3
Linac 1
Injector
Linac 2
Athos 0.7-7nm
Aramis 0.1-0.7 nm
BC1 0.38 GeV
BC2 2.1 GeV
3.0 GeV
3.0-5.8 GeV
user
stations
2.6-3.4 GeV
Linear accelerators
C-Band technology
Photocathode
RF gun
740m
  SwissFEL parameters
  Wavelength from 1 Å - 70 Å
  Photon energy 0.2-12 keV
  Pulse duration 1 fs - 20 fs
  e- Energy 5.8 GeV
  Repetition rate 100 Hz

## Slide 4: EEVR at PSI
EEVR functionality was developed in 2014 at PSI from protocol specification
Motivation
  Standalone systems without possibility of installing a hardware EVR.
  Some systems needed only limited timing functionality. 1 or 2 triggers for the FW or SW and the data buffer containing the machine pulse id was sufficient.
  Some applications need a specific functionality not provided in the standard EVR.
Available as
  VHDL component with TOSCA IF
  EDK Pcore with PLB
  Vivado IP Core with AXI Bus

## Slide 5: EEVR current state

## Slide 6: EEVR applications
The EEVR is used in various applications:
  BPMs
  LLRF system
  photon diagnostics
  experiments
The EEVR is used on different HW boards:

## Slide 7: Strategies for code reuse and collaboration
Modular design
  Source code for standard features provided by MRF
  Source code for custom features provided by collaboration
  Features selection by compilation parameters (generics)
EEVR - common VHDL components for all applications
  Wrappers are tool dependent and contain bus interfaces
MGT is part of user application
  MGT is FPGA dependent
  MGT reference clock configuration is application dependent
  Standardized interface between MGT and EEVR

## Slide 8: Collaboration in action

## Slide 9: Wir schaffen Wissen – heute für morgen
My thanks go to
Waldemar Koprek
Patric Bucher
Babak Kalantari