Open Source Event Receiver
Open Hardware Workshop EPICS Meeting
Argonne, June 2018
Jukka Pietarinen
Micro-Research Finland Oy

---
Open Source Event Receiver - Introduction
- What is the Open Source Event Receiver
  - Basic building block required to build devices receiving the MRF Timing protocol including but not limited to Delay Compensation capability
- What is it not
  - it is not a replacement firmware for current MRF products
  - it is not a complete Event Receiver with MRF product compatible register map
    - No bus/register interface
    - No pulse generators
    - etc.

---
Open Source Event Receiver - Requirements
- Hardware
  - Xilinx Kintex-7 based FPGA with GTX transceivers ONLY!
  - Zynq 7Z030 is Kintex-7 based
  - SFP Transceiver
  - Reference clock for GTX
  - Example design built for
    - Avnet PicoZed 7Z030
    - Avnet PicoZed FMC Carrier Card V2
- Software
  - Xilinx Vivado 2017.4 (Free WebPack version is sufficient)
- Xilinx programming cable
  - e.g. Platform Cable USB II

---
Avnet PicoZed FMC carrier with 7Z030 SOM
Avnet PicoZed AES-Z7PZ-7Z030-SOM-G
Avnet PicoZed FMC carrier AES-PZCC-FMC-V2-G
Zynq 7Z030 incorporates
Kintex-based FPGA core
Four GTX transceivers
Dual-core ARM Cortex-A9
This kit has everything from the hardware point of view to be used as an event receiver

---
Open Source Event Receiver - non-DC mode

---
Reference Design Structure
zynq_top.vhd - Design top level
  evr_dc.vhd - Event Receiver top level
    transceiver_dc_k7.vhd - GTX Transceiver instantiation
    delay_measure.vhd - Delay measurement
      average.vhd
    delay_adjust.vhd - DCM control
  databuf_rx_dc.vhd - Segmented data buffer receiver
    evr_pkg.vhd
    buf_bsram.vhd
zynq.xdc - Constraints file

---
Open Source Event Receiver
Clocks, reset
Event bus
Distributed bus
Receiver signals
Databuf bus
Transmitter signals
Delay compensation
signals

---
Minimum Configuration
- Connect reference clock to one reference clock input MGTREFCLKx_P/N
- Connect system clock to sys_clk
- Connect transceiver receive signals to MGTRX_P/N
- Tie databuf_rx_mode and databuf_tx_mode high ‘1’
- Tie dc_mode low ‘0’ (non-DC mode)
- Set delay_comp_target to a fixed value > 0x00050000, this value can be used to fine tune the “group delay” of the whole EVR. In non-DC mode this value sets depth of the EVR input FIFO.
- Tie other (unused) inputs low ‘0’

---
Receiving Events
- Event codes are presented on event_rxd in event_clk clock domain
- When event_rxd is not 0x00 there is an active event code
- link_ok can be used to check link status
if rising_edge(event_clk) then
if event_rxd = X”01” then
-- event code X”01” received
end if;
end if;

---
Receiving Distributed Bus Bits
- Distributed bus bits presented on dbus_rxd in event_clk clock domain
- When databuf mode is enabled dbus_rxd is updated every other clock cycle, when databuf mode is disabled dbus_rxd is updated every clock cycle
- link_ok can be used to check link status

---
Databuf bus
- Databuf bus is used to transfer data packets on databuf_rxd, databuf_rx_k, databuf_ena in event_clk clock domain
- Databuf mode has to be enabled

---
Sending Events
- Event codes are presented on event_txd in refclk clock domain
- When event_txd is not 0x00 the event code is sent out on the rising edge of refclk

---
Open Source Event Receiver - DC mode

---
Adding delay compensation
Bus interface
Databuf interface
Delay compensation signals
- delay_comp_update has to be connected to delay_comp_update of the evr_dc block
- delay_comp_rx has to be connected to delay_comp_value of the evr_dc block

---
Building Reference Design with Vivado
- Getting Sources
  - git clone https://github.com/jpietari/mrf-openevr
- Building Vivado project
  - cd mrf-openevr
  - vivado -mode tcl
    - Vivado% source ./openevr.tcl
    - Vivado% quit
- Synthesis/implementation/creating bitstream
  - Launch vivado in GUI mode
    - Vivado
      - Open project openevr/openevr.xpr
      - Generate bitstream
- FPGA configuration
  - Hardware manager
  - connect to target
  - download

---
Reference Design Features
- LEDs
  - LED1 (D6), rx_violation
  - LED2 (D7), link_ok
  - LED3 (D8), flashed quickly on received 0x01 event code
  - LED4 (D9), flashes slowly
- Pushbuttons
  - SW1 (N), rx_clear_violation
  - SW2 (S), tx_reset
  - SW3 (E), sys_reset
- The event link can be looped back to itself (connect fiber patch cable from SFP TX to SFP RX)
  - however due to GTX internals and running the transmitter and receiver from the same clock source you will need to press tx_reset several times before link gets established, this applies only to self-loopback. Theoretically, chances of establishing link is 1/20th resets.
- Sending out event code 0x01 at a fixed rate, few Hz, received event shows on LED3 (D8)
- Two integrated logic analyzer (ILA) cores instantiated

---
Avnet PicoZed FMC Carrier V2 Board Reference Clock
- Avnet PicoZed FMC Carrier V2 has a programmable IDT 8T49N242 clock synthesizer.
  - Configuration resides on an EEPROM
  - Reference design available from Avnet to program EEPROM
- Software Tools
  - IDT Timing Commander
  - IDT 8T49N24x Timing Commander Personality File
  - Xilinx Vivado and SDK 2015.4 (exact version required)
- Getting Sources
  - http://picozed.org/support/design/13076/106
  - Transceiver Clock Programming Reference Design

---
IDT Timing Commander

---
IDT Timing Commander
Copy table as a new configuration to file
C:\Avnet\hdl\Projects\pz_fmc2_valtest\software\pzcc_iic_eeprom_test\src\iic_eeprom_demo.c
Follow instruction in PizoZed_FMC2_Carrier_IDT_Clock_Programming_RefDes_2015_4.pdf

---
Evaluation Board Reference Clock
- Launch Vivado 2015.4
  - Open Project C:/Avnet/hdl/Projects/pz_fmc2_valtest/PZ7030_FMC2
  - Generate Bitstream
- Launch SDK 2015.4
  - Select Workspace C:\Avnet\hdl\Projects\pz_fmc2_valtest\PZ030_FMC2\pz_fmc2_valtest.sdk
  - Xilinx Tools -> Program FPGA, Click Program
  - Right-click pzcc_iic_eeprom_test
    - Run as -> Run Configurations
  - Click on Application tab
  - Search: pzcc_iic_eeprom_test.elf
  - Apply, Run

---
Further developments
- Adding more “bits and pieces” as configurable “plugins”
  - timestamping?
  - pulse generators?
  - bus interface for CPU access?
- Main idea is still to keep it as simple as possible
- VHDL is not a very convenient language for configurable designs - you have to use generate statements - no #ifdefs