## Slide 1: ALS-U: A major upgrade to the ALS
Bob Gunion
Lawrence Berkeley National Laboratory
June, 2018
1

## Slide 2: ALS-U Facility Status
Outline
  DOE Approval Status
  What is ALS-U
  Strategy

## Slide 3: DOE Approval Status
Currently at Conceptual Design stage, Reviews in progress
CD-0
Mission Need
Sept. 2016
CD-1
Conceptual Design
Fall 2018
CD-2
Performance Baseline
CD-3
Start Construction
CD-4
Completion
~2026
Dark Period <1 year
AR* Install
*AR = Accumulator Ring

## Slide 4: What is ALS-U
2-3 orders of magnitude brighter than ALS
Higher coherence due to lower emittance

## Slide 5: What is ALS-U
ALS-U: multi-bend achromat
ALS today : triple-bend achromat
Beam Size Comparison

## Slide 6: Bunch Train Swap-Out
  Swap-out enables:
  Stronger-focusing MBA lattices with smaller dynamic apertures
  Round beams - more useful shape and reduced emittance growth
  Vacuum chambers with small round apertures  Improved undulator performance
  Swap-out with full energy accumulator enables:
  Bunch train swap-out and recovery of the stored beam current
      Lower demand on the injector
      Very small (~nm) injected emittance
      More flexibility in fill patterns
Stored Beam
Injected Beam
Fast Kicker
Stored Beam
Injected Beam
Traditional off-axis injection
On-axis swap-out injection
(initially proposed by M. Borland)
requires larger
apertures
can use smaller
apertures
Only ALS-U and APS-U plan to include swap-out

## Slide 7: Project Scope
What’s New
Storage Ring (SR)
Accumulator Ring (AR)
Booster to AR Transfer Line (BTA)
AR to SR Transfer Line (ATS)
SR to AR Transfer Line (STA)
What Doesn’t Change
Gun
Linac
Booster
BTA
ATS
STA

## Slide 8: ALS-U Strategy
Re-use ALS systems
  Including recent & upcoming upgrades
Use Community Contributions
  EPICS7
  eTraveller & other tools
  Archiver Appliance
Follow other sites’ progress (APS-U)
Build new stuff when necessary
Plan for higher device count
  Possibly >1 million PVs vs. 200k for ALS
  Networking redesign

## Slide 9: Conclusions
ALS-U is a large and interesting project
The use of existing tools and expertise will be important for project success
New development will also be required
  We need people!
  http://jobs.lbl.gov, search by keyword

## Slide 10: Questions?

## Slide 11: Backup Slides

## Slide 12: Device Count
12
Power Supplies and Vacuum

## Slide 13: Scope of ALS-U
Existing ALS ring
New ALS-U ring
New accumulator ring
Retain the existing gun, linac, booster
Replace the existing triple-bend achromat storage ring with a new, high-performance storage ring based on a multi-bend achromat.
Add a low-emittance, full-energy accumulator ring in the existing storage-ring tunnel to enable on-axis, swap-out injection using fast magnets.
Replace the existing transfer line with new lines: BTA, ATS, STA

## Slide 14: ALS BPM Development
The ALS-U needs are,
192 in the storage ring (16 /sector)
72 in the accumulator ring (6 /sector)
~20 in the transfer lines
(We can reuse the present ALS SR BPMs (114) with a VCXO change)
160 built: 114 SR, 37 injector, and a few spares.
Mike Chin, Eric Norum, Greg Portmann, Jonah Weber at ALS and Kurt Vetter and others at NSLS-II

## Slide 15: Fast orbit feedback architecture
Fast Orbit Feedback Network (Dual 3.125 Gb/s fiber links)
Ethernet – pvAccess or Channel Access
MRF: Events / Timing Data (fiber fanouts)
PS1
PS2
PS3
PS4
PS5
PSn
Fast Feedback
Power Supplies
Cell
Controller
BPM1
BPM2
BPM3
BPM4
BPM5
BPMn
Beam Position
Monitors
Cell
Controller
...
Per Sector
Candidate Fast Power Supply for FOFB
(Caen Fast-PS Series)
Dual 3.125 Gb/s fiber links
1 Gb/s Ethernet fiber links

## Slide 16: Fast Magnet Count
BTA
STA
ATS
AR
SR
Decoherence kicker
AR kicker
SR kicker
NLK
Thin Septum
Thick Septum
BTA Lambertson
Septa
ATS/STA Lambertson Septa
Monitoring and Control Required
Timing
Controls
  HV Power Supplies (Enet)
  Interlocking (PLC)
Scopes
  6 channels @ 100 MHz
  18 channels @ 500 MHz

## Slide 17
Fast Orbit Feedback Network
Ethernet – pvAccess or Channel Access
Events / Timing Data
PLC
CNET
I /O
Field I/O
Field I/O
...
Controls Subnets (VLAN)
PLC
CNET
Field I/O
Field I/O
...
PLCs, Slow I/O, High Reliability, Low Accuracy, High Density. Used in Vacuum, slow EPS, non-FOFB PS, Cryo., Waterflow, Magnets, etc..
SIOC
Servers
I /O
Level 2: Operator stations: Displays, Archiving, Alarm Management, Strip charts, Save/Restore Utility
CPU
EVG
Timing Master
PS1
PS2
PS3
PS4
PS5
PSn
Fast Feedback
Power Supplies
Cell
Controllers
BPM1
BPM2
BPM3
BPM4
BPM5
BPn
RF
Systems
Beam Position
Monitors
Level 3: Physics or Science Applications Using Stored Data
Level 1: SCADA support over a distributed network
Level 0: High Performance Systems over dedicated networks (blue and orange) or slow control over industrial Ethernet
I /O
Standard HW Architecture
NAD
Power
Supplies
(Ethernet)
17