## Slide 1: Alarm System Update based on Apache Kafka
June 2018
Kay Kasemir
Evan Smith

## Slide 2: Evolution of CS-Studio
Since ~2010: Operational at several sites
Eclipse
Channels
PV Table
Probe
PV Tree
Data Browser
BOY
Scan
… more …
Alarms
Java 8
Phoebus
Channels
PV Table
Probe
PV Tree
Data Browser
Display Builder
Scan
… more …
Alarms
Java 9, 10
End of 2018 Goal: Some SNS beam lines
Eclipse
Channels
PV Table
Probe
PV Tree
Data Browser
Display Builder
Scan
… more …
Alarms
Java 8
Since ~2016: SNS beam lines, planned for ESS
SWT
JavaFX

## Slide 3: Alarm System
Alarm Server
  Monitor PVs
  Track alarms, acknowledgement
Alarm UI
  Configure (add PVs, guidance, links to displays)
  Show current state
  Acknowledge alarms
  Open guidance, related displays, email, log, ..

## Slide 4: Current Architecture
RDB
  Configuration
  Snapshot of last known state
JMS
  Acknowledge requests
  State updates
  Notification of configuration updates
/Accl/Vacuum: Guidance “…”
/Accl/Vacuum/PV1: Latch, last severity MINOR, time of last change, ..
/Accl/Vacuum/PV1: Severity now MINOR_ACK
/Accl/Vacuum: Guidance was changed
/Accl/Vacuum/PV1: Acknowledged

## Slide 5: Alarms: From RDB/JMS to Kafka
Clients need
  Config and initial state: RDB
  state updates: JMS
/Accl/Vacuum: Guidance “…”
/Accl/Vacuum/PV1: Latch, last severity MINOR, time of last change, ..
/Accl/Vacuum/PV1: Severity now MINOR_ACK
/Accl/Vacuum/PV1: {“severity”:”MINOR”, …}
/Accl/Vacuum/PV1: {“latch”:true, …}
/Accl/Vacuum: {“guidance”: …}
/Accl/Vacuum/PV1: {“severity”:”MINOR_ACK”, …}
 Do all that in Kafka?!
  Topic ‘Accelerator’ for configuration
  Topic ‘AcceleratorState’ for state

## Slide 6: Kafka stream for Alarms, ‘AcceleratorState’
From beginning of time, never ending
/Accl/Vacuum/PV1: {“severity”:”MINOR”, …}
/Accl/Vacuum/PV1: {“severity”:”MINOR_ACK”, …}
/Accl/Vacuum/PV1: {“severity”:”OK”, …}
/Accl/Vacuum/PV1: {“severity”:”MINOR”, …}
/Accl/Vacuum/PV1: {“severity”:”MINOR_ACK”, …}
/Accl/Vacuum/PV1: {“severity”:”OK”, …}
/Accl/RF/PV2: {“severity”:”MINOR”, …}
/Accl/RF/PV3: {“severity”:”MAJOR”, …}
/Accl/RF/PV2: {“severity”:”OK”, …}
Clients tend to only need the most recent state for each item, followed by updates
…
…
Time

## Slide 7: Kafka Storage of ‘AcceleratorState’…
New ‘segment’, e.g. every 10 seconds..
Time
…
/Accl/Vacuum/PV1: {“severity”:”MINOR”, …}
/Accl/Vacuum/PV1: {“severity”:”MINOR_ACK”, …}
/Accl/Vacuum/PV1: {“severity”:”OK”, …}
/Accl/Vacuum/PV1: {“severity”:”MINOR”, …}
/Accl/Vacuum/PV1: {“severity”:”MINOR_ACK”, …}
/Accl/Vacuum/PV1: {“severity”:”OK”, …}
/Accl/RF/PV2: {“severity”:”MINOR”, …}
/Accl/RF/PV3: {“severity”:”MAJOR”, …}
/Accl/RF/PV2: {“severity”:”OK”, …}
Simply delete older segments?
Then state of PV3 is lost..

## Slide 8: ‘Compacted’ Kafka ‘AcceleratorState’
Keeping single older segment w/ last value for each item
…
New clients get at least the most recent state for each item, maybe a few more,
followed by updates
/Accl/Vacuum/PV1: {“severity”:”OK”, …}
/Accl/Vacuum/PV1: {“severity”:”MINOR”, …}
/Accl/Vacuum/PV1: {“severity”:”MINOR_ACK”, …}
/Accl/Vacuum/PV1: {“severity”:”OK”, …}
/Accl/RF/PV2: {“severity”:”MINOR”, …}
/Accl/RF/PV3: {“severity”:”MAJOR”, …}
/Accl/RF/PV2: {“severity”:”OK”, …}
Time

## Slide 9: Initial Tests
2010 Test (PosgreSQL, JMS)
Load hierarchy with 50000 PVs into RDB
  5 minutes
Show config in new Alarm Tree
  Nothing shown until all loaded after 30 seconds
Handle Alarm Updates
  10 per second
2018 Test (Kafka)
100000 PVs into Kafka
  3 seconds
  Shows growing tree for 10 seconds
  500 per second

## Slide 10: State of Development
Functional
  Alarm Server
  Import/Export of XML-based configuration
    Same format as before
  Alarm Tree
    Configure, monitor, acknowledge, ..
  Alarm Table
    Primary operator view of current alarms
  Area Panel
    For cross-the-room status check
To Do
  Annunciator
  Authentication for changes

## Slide 11: Further Ideas for - based Alarm System
Stream ‘compacted’ alarm topics into
  Non-compacted Kafka Topics: Long-term history
  RDB, MongoDB, ElasticSearch: Alternate long-term history, existing tools to analyze
For what it’s worth: ESS uses Kafka to stream EPICS PVs & Instrument data,
http://accelconf.web.cern.ch/AccelConf/icalepcs2017/papers/tupha177.pdf

## Slide 12: Alarm System Update for Phoebus
RDB & JMS 
Same XML import/export
Similar UI
Performance headroom

## Slide 14: Other Changes
Server now ‘maximizes’ severity of all nodes up to root
  Used to be in client
  Has to be in server to support ‘sevr_pv’
  A little more traffic, but
    simpler client code
    more information for reports, statistics, dashboards

## Slide 15: Quirks (not show stoppers)
Deleting and then re-creating a topic to “start over” causes log cleaner to quit. Need to restart Kafka.
“Delete” alarm tree node.. means adding a null entry. New clients often see both messages, i.e. add and soon delete the entry. Full cleanup means starting over: Export data, recreate topic (requires Kafka restart), import data.
/Accl/Vacuum/PV1: {“latch:true, …}
/Accl/Vacuum/PV1: null