## Slide 2
Context
IOC
Input Output Controler
PLC
Programmable Logic Controler
Data block communication

## Slide 3
Context
IOC
Input Output Controler
PLC
Programmable Logic Controler
Data block communication

## Slide 4: CEA context
5 projects per year with PLC
From 200 to 6000 variables
Need a programming communication solution for non EPICS developer
“Light” automatic solution

## Slide 5
SOLUTION
IOC
Input Output Controler
PLC
Programmable Logic Controler
Data block communication
Automatic generation

## Slide 6: S7PLC protocol example
TIA Portal: 2 awl files that contains 3 information: name, type, description
Application:
  Calculate data offset in data block message
  Add EPICS fields: SCAN, alarm, PINI
  Possibility to add other fields
  Communication: @IP, port, timeout,…

## Slide 7: S7PLC protocol example
Export TIA Portal

## Slide 8: S7PLC protocol example
Export TIA Portal
DATA_BLOCK "DATA_RECV_FROM_EPICS"
TITLE = SKID, Proj_Skid,,
{ S7_Optimized_Access := 'FALSE' }
AUTHOR : Joannem
FAMILY : ComEPICS
NAME : S7_PLC
VERSION : 0.1
NON_RETAIN
STRUCT
"SKID:PLC-001:R10P" : Real; // Regulation P
"SKID:PLC-001:R10I" : Real; // Regulation I
"SKID:PLC-001:R10U" : Real; // Regulation U
…
ENDSTRUCT;
SKID: name of EPICS IOC
Proj_Skid: PLC name in S7PLC

## Slide 9: S7PLC protocol example
Import awl file: choose protocol

## Slide 10: S7PLC protocol example
Import awl file: choose file

## Slide 11: S7PLC protocol example
Import awl file: Define communication parameters

## Slide 12: S7PLC protocol example
Default EPICS parameters : SCAN, ZNAM, ONAM, ZSV, OSV

## Slide 13: S7PLC protocol example
Add new EPICS field

## Slide 14: S7PLC protocol example
Tricks
  Search variable
  Right click: Hide column, delete columns
  Display hide columns
  Sorting and unsorting by columns

## Slide 15: S7PLC protocol example
Generate IOC

## Slide 16: S7PLC protocol example
Generate IOC: display new parameters, change, and deleted

## Slide 17: S7PLC protocol example
Generate IOC:
  iocBoot/iocSkid/boot/iocTest.cmd
  iocBoot/iocSkid/src/iocTestInclud.dbd
  iocBoot/iocSkid/src/Makefile
  skidApp/db/skid.db
  skidApp/db/Makefile

## Slide 18: S7PLC protocol example
Generate IOC: db file
  #! DBDSTART
  #! DBDEND
  record(ao, "SKID:PLC-001:R10P"){
  field(PINI, "YES")
  field(DTYP, "S7plc")
  field(DESC, " Regulation - PP10 - KP")
  field(OUT, "@Proj_Skid/0 T=FLOAT")
  }
  record(ao, "SKID:PLC-001:R10I"){
  field(PINI, "YES")
  field(DTYP, "S7plc")
  field(DESC, " Regulation - PP10 - TI")
  field(OUT, "@Proj_Skid/4 T=FLOAT")
  }
  …

## Slide 19: TODO
TODO:
  Bugs resolution in progress like calculation of inSize and outSize
  Better merge
  Better design: Model View Controller
  Standalone without Eclipse
  Modbus/TCP

## Slide 20: Generate IOC communication for Siemens PLC
Thanks for your attention